## Slide 1
Sectoral findings and results
for the Mineral Industry
2° Workshop on National Action Plan for Green Transition in Industry
29 November 2023

## Slide 2: Sub-Activities of the Mineral Industry under IED Annex I
Sub-Activity Codes | Identification of activities
Mineral Industry | 
3.1 | Production of cement, lime and magnesium oxide (a) Production of cement clinker in rotary kilns with a daily production capacity of more than 500 tons or in other kilns with a daily production capacity of more than 50 tons (b) Production of lime in furnaces with a daily production capacity of more than 50 tons (c) Production of magnesium oxide in furnaces with a daily production capacity of more than 50 tons
3.2 | Manufacture of asbestos or asbestos-based products *
3.3 | Glass and fiberglass production with a melting capacity of over 20 tons per day
3.4 | Melting of minerals and production of mineral fibers with a melting capacity of more than 20 tons per day
3.5 | Production of ceramic products, especially tiles, bricks, refractory bricks, durable pots, pottery, ceramic tile or porcelain by firing method with a production capacity of more than 75 tons per day and/or an furnace capacity exceeding 4 m3 and a density of more than 300 kg/m3 per furnace
* Forbidden in Türkiye | 

## Slide 3: BREF Documents Covering Sub-sectors of Mineral Industry
Cement, Lime and Magnesium Oxide Production BREF Document (CLM BREF)
Glass Manufacturing BREF Document (GLS BREF)
Ceramic Manufacturing Industry BREF Document (CER BREF)

## Slide 4: Cement Production
Production of cement, lime and magnesium oxide is all included in the IED Annex I with 3.1 code.
3.1. Production of cement, lime and magnesium oxide:
3.1(a) Production of cement clinker in rotary kilns with a daily production capacity of more than 500 tons or in other kilns with a daily production capacity of more than 50 tons

## Slide 5: Main Environmental Issues
Emissions released into the air and energy usage are the main environmental issues related to cement production.
Wastewater discharge is generally only limited to surface runoff and cooling water, and does not make a significant contribution to water pollution. However, the storage and transportation of fuels is a potential source of soil and groundwater pollution.

## Slide 6: Sectoral Transition for the Cement Sector according to the EÇİ (Integrated Environmental Permit) Project
A project titled 'Determination of Compliance Situations and Requirements of Cement Factories Subject to Integrated Environmental Permit' was carried out for this sector between 2015-2017. Within the scope of the project, 54 cement plants were evaluated to determine their compliance status with the IED, investment needs for the implementation of the BATs and the time required for the sectoral transition.
In addition to the compliance cost assessment, a sectoral transition calendar was determined for the Turkish cement industry in the EÇİ (Integrated Environmental Permit) Project. According to the report prepared by the project team at that time, flexible and gradual IED transition was proposed according to scenarios between 1 and 7 years.

## Slide 7: Results of Compliance and Cost Assessment of the Cement Sector
Sector | Number of facilities | Average compliance rate (%) | Average CAPEX (EURO)
3.1(a) | 56 | 59 | 916.000.000
Considering that the transition period foreseen in 2017 (five years) in the cement sector has passed and the obligations brought by CBAM are taken into account, the transition period is estimated to be three years from now.

## Slide 8: Production of Lime and Magnesium Oxide
Industrial activities covered under IED Annex I for the lime and magnesium oxide sectors are specified in the following sections:
3.1. Production of cement, lime and magnesium oxide:
  3.1(b) Production of lime in furnaces with a daily production capacity of more than 50 tons,
  3.1(c) Production of magnesium oxide in furnaces with a daily production capacity of more than 50 tons

## Slide 9: Main Environmental Issues
The main environmental issues related to lime production are that it involves processes that generate air pollution and use intensive energy. Lime burning and the secondary processes of lime: quenching and grinding are the main sources of emissions and the most critical energy users. In lime production, important air emissions such as carbon oxides (CO, CO2), NOx, SO2 and dust (PM) occur during the calcination phase.
Similarly, the energy-intensive combustion process and emissions to air are the two most critical environmental challenges in producing various forms of magnesium oxide. Burning of magnesium, secondary grinding and other processes such as crushing, sieving, transporting, storing and unloading can have a significant environmental impact. The main source of emissions to air in magnesia production is combustion, where dust, NOx, SO2 and CO are produced. These emissions are partly due to the properties of the raw material magnesite and partly due to the fuels used. SO2 emissions from the raw material (magnesite) are affected by the sulfur level in the mineral.

## Slide 10: Results of Compliance and Cost Assessment of the Lime Sector
According to the IPPC Inventory, there are 69 plants regarding the lime production in Türkiye. Based on the answers received to the BAT CL survey, the overall compliance for the sector was calculated at 37%.
Sub-sector | Average Compliance % | Number of Plant | Min. CAPEX (EURO) | Max. CAPEX (EURO) | Min. OPEX (EURO/year) | Max. OPEX (EURO/year)
3.1.b (Lime) | 37 | 69 | 456.000.000 | 1.436.000.000 | 216.000.000 | 320.000.000

## Slide 11: Results of Compliance and Cost Assessment of the Magnesium Oxide Sector
Regarding the production of magnesium oxide, there are 22 plants in Türkiye according to the IPPC inventory. Based on the answers received to the BAT CL survey, the overall compliance for the sector was calculated at 44%.
Sub-sector | Average Compliance % | Number of Plant | Min. CAPEX (EURO) | Max. CAPEX (EURO) | Min. OPEX (EURO/year) | Max. OPEX (EURO/year)
3.1.c | 44 | 22 | 141.000.000 | 247.000.000 | 37.000 | 123.000

## Slide 12: Glass Production
For the Glass Sector, the industrial activities within the scope of IED Annex I are specified in the following section:
3.3. Glass and fiberglass production with a melting capacity of over 20 tons per day;
3.4. Melting of minerals and production of mineral fibers with a melting capacity of more than 20 tons per day

## Slide 13: Main Environmental Issues
The main environmental issue with the production of different types of glass is related to the high-temperature, energy-intensive. Due to the high-temperature oxidation of atmospheric nitrogen and the emissions of combustion products to the air, carbon dioxide, NOx and sulfur dioxide are produced. Particulate matter, fluorides and chlorides, and in some cases metals, result from high-temperature evaporation and possible recondensation of the volatile compounds contained in the raw materials, either intentionally used in the batch formulation or due to impurities of the raw materials.

## Slide 14: Results of Compliance and Cost Assessment of the Glass Sector
According to the IPPC inventory, there are 42 glass production plants in Türkiye. Based on the answers received to the BAT CL survey, the overall compliance of the sector was calculated at 56%.
Sub-sector | Average Compliance % | Number of plants | Min. CAPEX (EURO) | Max. CAPEX (EURO) | Min. OPEX (EURO/year) | Max. OPEX (EURO/year)
3.3 & 3.4 | 56 | 42 | 152.000.000 | 1.542.000.000 | 7.000.000 | 210.000.000

## Slide 15: Ceramic Production
For the Ceramic Sector, the industrial activities within the scope of IED Annex I are specified in the following section:
3.5. Production of ceramic products by firing, in particular roofing tiles, bricks, refractory bricks, tiles, stoneware or with a production capacity of more than 75 tons per day and/or with a kiln capacity exceeding 4 m3 and with a setting density per kiln of more than 300 kg/m3

## Slide 16: Main Environmental Issues
Emissions released to the air: particulate matter/dust, soot, gas emissions (carbon oxides, NOx, SOx, inorganic fluorine and chlorine compounds, organic compounds and heavy metals).
Emissions released to water: process wastewater mainly contains minerals (insoluble particulate matter) and other inorganic components, as well as trace amounts of numerous organic substances and some heavy metals.
Process losses/wastes: Most of the process wastes caused by the production of ceramic products consist of various types of mud, broken pots, used plaster molds, used absorbents, solid residues (dust, ash) and packaging wastes.
Energy consumption/CO2 emissions: All sectors of the ceramic industry use a lot of energy because firing the ceramics at temperatures between 800 and 2000 oC after drying is the most important step in the process.

## Slide 17: Results of Compliance and Cost Assessment of the Ceramic Sector
According to the IPPC inventory, there are 310 ceramic production plants in Türkiye. Based to the answers received to the BAT CL survey, the overall compliance for the sector was calculated at 40%.
Sub-sector | Average Compliance % | Number of plants | Min. CAPEX (EURO) | Max. CAPEX (EURO) | Min. OPEX (EURO/year) | Max. OPEX (EURO/year)
3.5 | 40 | 310 | 1.109.000.000 | 3.893.000.000 | 70.000.000 | 603.000.000

## Slide 18: General Compliance and Cost Assessment for the Mineral Sector
In general, it can be said that the energy-intensive and high-temperature process for the mineral sector leads to a significant amount of air emissions from the melting furnaces and kilns: greenhouse gas emissions, dust, NOx, SOx, HCl, HF, metals etc., as well as fossil fuel consumption and process emissions (CO2 from the decomposition of carbonates). Currently, although the reduction of energy consumption is included under the IED, greenhouse gas emissions are not included.
According to IPPC inventory, there are 499 plants within the scope of the mineral sector in Türkiye. The overall average compliance rate, covering the entire mineral sector, is observed at 43%.

## Slide 19
Sub-sectors | CAPEX (Total, EURO) | OPEX (Total, EURO/year) | Transition period (year) | 2024-2026 Investment requirement (3 years) (EURO) | 2027-2030 Investment requirement (3 years) (EURO) | 2030-2032 Investment requirement (3 years) (EURO)
3.1.a Cement production | 916.000.000 | - | 3 | 916.000.000 | - | -
3.1.b Lime production | 946.000.000 | 268.000.000 | 6 | 473.000.000 | 473.000.000 | -
3.1.c MgO production | 194.000.000 | 80.000 | 3 | 194.000.000 | - | -
3.3 & 3.4 Glass and mineral wool production | 847.000.000 | 108.500.000 | 6 | 423.500.000 | 423.500.000 | -
3.5. Production of ceramic | 2.501.000.000 | 336.500.000 | 9 | 833.670.000 | 833.670.000 | 833.670.000
TOTAL | 5.404.000.000 | 713.080.000 | 3-9 | 2.840.170.000 | 1.730.170.000 | 833.670.000

## Slide 20
Thank you